| INTERNATIONAL TELECOMMUNICATION UNION |  |
| --- | --- |
|  | RRC-06 | REGIONAL RADIOCOMMUNICATION CONFERENCE (SECOND SESSION) | Addendum 3 to Document 7-E |
|  |  |  | 17 February 2006 |
|  |  |  | Original: English/ French/ Russian/ Spanish |
| GENEVA, 15 MAY – 16 JUNE 2006 |  |
|  | PLENARY MEETING |
| EUROPEAN COMMON PROPOSALS FOR THE WORK OF THE CONFERENCE |
| Part 3 Annex 2 to the Agreement: Technical criteria used in the development of the Plan and the implementation of the Agreement |

Agenda item of Resolution 1224 of the ITU Council: resolves 2.1.1

# Introduction

In accordance with ITU Council Resolution 1224, the Conference will produce frequency plans associated with the new Agreement, as described in §5.1.1.2 of the report of the first session, for terrestrial digital broadcasting in the frequency bands 174-230 MHz and 470-862 MHz.

The RRC-06 Agreement will, as the previous agreements Stockholm 1961 and Geneva 1989, contain an Article which deals with the modification of the Plans. This Article will also address the coordination of stations of other primary terrestrial services against the Plans. Technical provisions are needed to describe the criteria and parameters to be applied for modifications of the Plans and the coordination of stations of other primary terrestrial services against the Plans.

During the transition period, there is a need to have technical provisions for modifications to the Plans not only for the digital to digital case but also for digital to analogue, analogue to digital and analogue to analogue.

Mandatory references to ITU-R Recommendations used in the technical provisions must be to the specific Recommendations in force at the date of the adoption of the Plans. It is proposed not to reproduce these Recommendations in the Agreement or its annexes but to include the full text of the Recommendations in an attachment to the Agreement.

The procedures and the associated technical criteria and parameters for the modification of the analogue plan shall not be applied after the transition period.

# Proposal

EUR/7A3/1

The Agreement shall include procedures for the modification to the Plans and for the coordination of other primary terrestrial services; these procedures shall refer to an annex containing the relevant technical criteria and parameters.

a)	The following cases must be taken into account:

- when modifying the Plans:

For the broadcasting service against broadcasting service

Digital – Digital

Digital – Analogue

Analogue – Digital

Analogue – Analogue

For the broadcasting service against other primary terrestrial services

Analogue broadcasting service – Other primary terrestrial services

Digital broadcasting service – Other primary terrestrial services

- for the coordination of stations of other primary terrestrial services against the Plans:

Other primary terrestrial services – Analogue broadcasting service

Other primary terrestrial services – Digital broadcasting service

b)	The technical annex should include the cases described in a) above.

c)	The technical annex shall be part of the Agreement and it shall only include the values needed for the modifications to the Plans and the coordination of stations of other primary terrestrial services with the Plans. A proposed structure of Annex 2 to the Agreement is shown in Attachment 1 to this present document.

d)	Mandatory references to ITU-R Recommendations used in the technical provisions shall be to specific  Recommendations in force at the date of the adoption of the Plans.

- It is proposed not to reproduce these Recommendations in the Agreement or its annexes, but to include the full text of the Recommendations in an Attachment to the Agreement to be published electronically only.

# Reason

To have a self consistentAgreement.

Attachment 1

Structure of Annex 2 of the Agreement

ANNEX 2: Technical criteria used in the development of the Plan and the implementation of the Agreement

Chapter 1	Definitions

Chapter 2	Propagation in the VHF/UHF Bands

Chapter 3	Technical basis for establishing and modifying the terrestrial broadcasting Plan (T-DAB and DVB-T)

Chapter 4	Technical basis for sharing between the Broadcasting Service and Other Primary Terrestrial Services within the same frequency band

N.B.  Addenda to this ECP will include the contents of these chapters

# Footnotes

this case is generally not covered due to the lack of values available in ITU-R Recommendations.